## Slide 1
Introduction to data communications
Lecturer: Itamar Cohen
Chapter 4: the network layer
Part 1: packets and routers
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
Based on slides by J.F Kurose and K.W. Ross, all Rights Reserved All material copyright 1996-2012

## Slide 2
Introduction
Virtual circuits
Datagram networks
What’s inside a router
Outline

## Slide 3: Network layer
transport segment from sending to receiving host
on sending side encapsulates segments into datagrams
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Two key network-layer functions
forwarding: move packets from router’s input to appropriate router output
routing: determine route taken by packets from source to dest.
  routing algorithms
analogy:
routing: process of planning trip from source to dest
forwarding: process of getting through single interchange

## Slide 5
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
Interplay between routing and forwarding
routing algorithm determines
end-end-path through network
forwarding table determines
local forwarding at this router

## Slide 6
Introduction
Virtual circuits
  Motivation
  Implementation
Datagram networks
What’s inside a router
Outline

## Slide 8
Guaranteed delivery
  Preferably within a bounded delay
Guaranteed minimum bandwidth to flow
In-order datagram delivery
Restrictions on changes in inter-packet spacing (jitter)
Security
The Internet guarantees none of these!
“Nice-to-have” network services

## Slide 9
Introduction
Virtual circuit
  Motivation
  Implementation
    ATM
    VPN & MPLS
    Principles of circuit switching
Datagram networks
What’s inside a router
Outline

## Slide 11
Designed to handle well both high-TP apps and RT apps
Used over backbone optical networks and Integrated Services Digital Networks
Obsolete
Asynchronous Transfer Mode

## Slide 12
ATM is parallel to the 3 bottom layers in ISO model
ATM may be thought as a hybrid of pkt-switching and circuit-switching
Use small, fixed-size packets (cells)
  Like packet swithicng
Use connection setup, which builds a virtual circuit
  Like circuit switching
Asynchronous Transfer Mode - principles

## Slide 13: Network layer service models
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?
Notes: Constant Bit Rate
Available Bit Rate: an average or Sustainable Cell Rate is specified. The rate can reach at most a pre-specified Peak Cell Rate, for a bounded interval.
Variable Bit Rate
Unspecified Bit Rate

## Slide 14
Introduction
Virtual circuit
  Motivation
  Implementation
    ATM
    VPN & MPLS
    Principles of circuit switching
Datagram networks
What’s inside a router
Outline

## Slide 15
Motivation: allow enterprise a secure, private connection over a public Wide Area Network
  Large distances
  Possibly wireless
  Use proxy servers to improve privacy
Use tunneling and / or encryption
Tunnel’s termination points
are located either at
  Customer edge
  ISP’s edge
Virtual Private Network

## Slide 16
Security is implemented by either
  App layer: Secure Shell (ssh) – which allows security over an unsecure network
  Transport layer (at end-hosts): Secure-Socket Layer
  Network layer: encapsulate
  an IP packet within
  an encrypted IPSec packet
Virtual Private Network: Security
Notes:   In addition: Legacy protocols by Cisco, Microsoft

## Slide 17
VPN may be routed using Multi Protocol Label Switching
MPLS is good also for
  Traffic Engineering
  Out-Of-Band control
  Centralized SDNs:
  Software
  Defined
  Networks
Virtual Private Network: Routing

## Slide 18
 Improved privacy and security
  As required by VPNs
 No need for expensive, complicated routing algorithms and routing tables
 Easier Traffic Engineering
 Out-Of-Band control
Usages
  Virtual Private Networks
  Centralized Software Defined Networks
 Requires packets [En | de] capsulation
 Central control is complex, not scalable and subject to failures
 Requires connection setup
Multi Protocol Label Switching

## Slide 19: IP Datagrams on Virtual Circuits: Data Center Networks
Typical traffic pattern in Data Center
  Most of the congestion is caused by few long lived flows (elephants)
  Many short lived flows (mice)
  Use virtual circuits either for…
    all flows
    only elephants
      Mice use normal IP forwarding
      Problem: how to identify elephants?

## Slide 20
Introduction
Virtual circuit
  Motivation
  Implementation
    ATM
    VPN & MPLS
    Principles of Virtual Circuits
Datagram networks
What’s inside a router
Outline

## Slide 21: Call setup
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
every router on source-dest path maintains “state” for each passing connection
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
“source-to-dest path behaves much like telephone circuit”
  performance-wise
  network actions along source-to-dest path

## Slide 22: VC implementation
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  new VC number comes from forwarding table

## Slide 23: VC forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!

## Slide 24: Virtual circuits: signaling protocols
application
transport
network
data link
physical
used to setup, maintain, teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical

## Slide 25
Introduction
Virtual circuit
Datagram networks
What’s inside a router
Outline

## Slide 26: Connection, connection-less service
datagram network provides network-layer connectionless service
virtual-circuit network provides network-layer connection service
analogous to TCP/UDP connection-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 27: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 28: Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 29: Datagram Vs Virtual Circuits
Internet (datagram)
data exchange among computers
  “elastic” service, no strict timing req.
many link types
  different characteristics
  uniform service difficult
Distributed control
ATM (VC)
evolved from telephony
human conversation:
  strict timing, reliability requirements
  need for guaranteed service
Central control

## Slide 30: Source Routing
Alternative to Virtual Circuits and usual packet routing
The idea: list entire path in packet
  Driving directions (north 3 hops, east, etc..)
Router processing
  Examine first step in directions
  Strip first step from packet
  Forward to step just stripped off
Receiver
Packet
R2, R3, R
Sender
2
3
4
1
2
3
4
1
2
3
4
1
R2
R3
R1
R3, R
R

## Slide 31: Source Routing
Advantages
  Switches can be very simple and fast
Disadvantages
  Variable (unbounded) header size
  Sources must know or discover topology (e.g., failures)
Notes: Typical use
  Ad-hoc networks (DSR)
  Machine room networks (Myrinet)

## Slide 32: VC / IP address / source routing
Source Routing
Global Addresses
Header Size
Worst
OK – Large address
Router Table Size
None
Number of hosts (prefixes)
Forward Overhead
Best
Prefix matching
Virtual Circuits
Best
Number of circuits
Pretty Good
Setup Overhead
None
None
Error Recovery
Tell all hosts
Tell all routers
Connection Setup
Tell all routers and Tear down circuit and re-route

## Slide 33
Introduction
Virtual circuits
Datagram networks
What’s inside a router
  Architecture overview
  Input ports
  Switching fabric
  Output ports
  Present & future trends
Outline

## Slide 34: Router architecture overview
two key router functions:
run routing algorithms/protocols
forwarding datagrams from incoming to outgoing link
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 35
Introduction
Virtual circuit
Datagram networks
What’s inside a router
  Architecture overview
  Input ports
  Switching fabric
  Output ports
  Present & future trends
Outline

## Slide 36: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet,
WiFi
switch
fabric

## Slide 37: Forwarding table
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?

## Slide 38: Longest Prefix Matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 39: Address Lookup: Binary Tries
Example Prefixes:
a) 00001
b) 00010
c) 00011
d) 001
e) 0101
f) 011
g) 100
h) 1010
i) 1100
j) 11110000
e
f
g
h
i
j
0
1
a
b
c
d

## Slide 40: Address Lookup: TCAM
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
Link interface
0
1
2
3
(Ternary) Content Addressable Memory

## Slide 41: Input port queuing and HoL blocking
Speedup=k: at each cycle:
  Each input queue can transfer at most k packets
  Each output queue can accept at most k packets
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
When speedup=1 the green packet experiences HoL blocking
switch
fabric

## Slide 42
Introduction
Virtual circuit
Datagram networks
What’s inside a router
  Architecture overview
  Input ports
  Switching fabric
  Output ports
  Present & future trends
Outline

## Slide 43: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
Shared
memory
bus
crossbar

## Slide 44: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 45: Switching via interconnection network
Overcome bus bandwidth limitations
Solutions to the scalability problem
  Hierarchical Xbar
  Fragmenting datagram into fixed length cells, switch cells through the fabric
  Sophisticated (perfect / wegihted) matching algorithms
crossbar

## Slide 46: Switching fabrics
Transfer packet from input buffer to appropriate output buffer
Most common implementation: Xbar
Speedup=k: at each cycle:
  Each input queue can transfer at most k packets
  Each output queue can accept at most k packets
By default, speedup=1
A work conserving algorithm: if at some cycle there’s a packet destined to output port j, then at cycle, output port will transmit a packet
  Very hard to guarantee
  Can mitigate non-conserving cycles using VOQs and / or speedup > 1
crossbar

## Slide 47
Introduction
Virtual circuit
Datagram networks
What’s inside a router
  Architecture overview
  Input ports
  Switching fabric
  Output ports
  Present & future trends
Outline

## Slide 48: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 49: Output queuing: buffer size
The “rule of thumb” (RFC 3439):
Buffer size = RTT * BW
  Intuition: assume “full TCP window”
  e.g., BW = 10 Gpbs, RTT=250ms  Buff 2.5 Gb
  Major improvement [Keslassy et. al]: when there’re N flows destined to the same output, buffering equal to
  is “enough”
RTT BW
.
N

## Slide 50: Output queuing: max-min fairness
Consider 4 clients, with demands: 2, 2.6, 4, 5
Capacity: 10
How to allocate the capacity fairly?
A one minute film showing the exact calculation

## Slide 51: Output queuing: scheduling
Round Robin
Weighted Round Robin
Generalized Processor Sharing (“bitwise RR”)
Weighted Fair Queuing
Deficit Round Robin

## Slide 52
Introduction
Virtual circuit
Datagram networks
What’s inside a router
  Architecture overview
  Input ports
  Switching fabric
  Output ports
  Present & future trends
Outline

## Slide 53: Router Chassis
Cisco GSR 12816
Juniper T640
2m
50 cm
60cm
Capacity: 640Gb/s Power: 5kW
1m
75 cm
50 cm
Capacity: 320Gb/s Power: 3kW

## Slide 54: Router Design
Many trade-offs: power, $$$, throughput, reliability, flexibility
Important bottlenecks on fast path
  Longest prefix match
  Cross-bar scheduling
Trends: Central control  distributed control
  High-end HW routers
and… back to centralized control
  Software Defined Networks
and… back again to dist’ control
  Edge computing

## Slide 55: Network Processors: motivation
Motivation: Packets should pass through multiple processing stages
  IP lookup & forwarding
  Header updating
    Time To Live
    Error Congestion Notification
    Re-calculation of Checksum
  Filtering
  Deep Packet Inspection
  Multi-Protocol Label Switching [en|de]capsulation
  [En|de]cryption
Software: too slow
Hardware: not flexible

## Slide 56: Network Processors
Combination of Software-Hardware
Multi-phase pipelined / parallel processing
Challenges
  Variable processing time
  Variable gains from packets
  Processing-time and gain from packet not necessarily known when it arrives