## Slide 1
Introduction to data communications
Lecturer: Itamar Cohen
Chapter 4: the network layer
Part 2: IP
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
Based on slides by
  Dr. Yoram Haddad, JCT
  J.F Kurose and K.W. Ross, all Rights Reserved
All material copyright 1996-2012

## Slide 2: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router signaling
transport layer: TCP, UDP
link layer
physical layer
network
layer

## Slide 3
IPv4 Header format
IPv4 addressing
ICMP
IPv6
Outline

## Slide 4: IPv4 Header
Notes: DSCP – Differentiated Service Code Point – used for QoS. Replaces the outdated Type of Service.
IHL – Internet Header Length – size of the IP hdr (in 32-b words).
ID – used for identifying fragments of the same seg’.
Flags: reserved; don’t fragment; more fragments.
Prot’: TCP, UDP, DCCP; ICMP, OSPF, IGRP (private intra-AS routing prot’), IP-in-IP (encap’), IGMP, …

## Slide 5: Fragmentation & Reassembly
Max Transfer Unit differs among various link types
When needed, a large IP datagram is fragmented
and reassembled at final destination
IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 6: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 7
Header format
IPv4 addressing
  Subnets and prefixes
  DHCP
  NAT
ICMP
IPv6
Outline

## Slide 8: IPv4 addressing: introduction
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 9: Subnets
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 10: Subnet mask
The mask is the longest prefix (starting from the MSB) which is common to all hosts in the same subnet
subnet mask: /24
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 11: Address aggregation

## Slide 12: Address aggregation

## Slide 13: Longest mask matching
Notes: Explanation for R2’s Routing table:
First row:
Org 4: 1000_1100 . 0001_1000 . 0000_0111 . 11XX_XXXX
Row 2:
Org 1: 1000_1100 . 0001_1000 . 0000_0111 . 00XX_XXXX
Org 2: 1000_1100 . 0001_1000 . 0000_0111 . 01XX_XXXX
Org 3: 1000_1100 . 0001_1000 . 0000_0111 . 10XX_XXXX
Row 3: “To other networks” at the diagram.
Row 4: Default Router.

## Slide 14: Longest mask matching
R4
140.24.6.0/24
R1
R2
R3
R4
Notes: R2’s Routing table
/24 1000_1100 . 0001_1000 . 0000_0110 . XXXX_XXXX, R3, m1
/26 1000_1100 . 0001_1000 . 0000_0111 . 11XX_XXXX, R3, m1
/24 1000_1100 . 0001_1000 . 0000_0110 . XXXX_XXXX, R1, m0
/0 0.0.0.0, R4, m2
R3’s Routing table
/24 1000_1100 . 0001_1000 . 0000_0110 . XXXX_XXXX, -, m1
/26 1000_1100 . 0001_1000 . 0000_0111 . 11XX_XXXX, -, m0
/0 0.0.0.0, R2, m2

## Slide 15: Longest mask matching
R4
140.24.6.0/24
R1
R2
R3
R4
Notes: Explanation for R2’s Routing table:
First row:
Org 4: 1000_1100 . 0001_1000 . 0000_0111 . 11XX_XXXX
Row 2:
Org 1: 1000_1100 . 0001_1000 . 0000_0111 . 00XX_XXXX
Org 2: 1000_1100 . 0001_1000 . 0000_0111 . 01XX_XXXX
Org 3: 1000_1100 . 0001_1000 . 0000_0111 . 10XX_XXXX
Row 3: “To other networks” at the diagram.
Row 4: Default Router.

## Slide 16: Subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 17: Classful addressing (obsolete)
In the past, IP addresses were divided to classes, with fixed-size prefixes of 8,16 or 24 bits
  E.g. a class with prefix of only 8 bits was huge – allowing ___ devices in it
This led to significant waste of IP addresses, which were allocated to classes, and therefore was replaced by CIDR (see next slide)

## Slide 18: Classless Inter Domain Routing
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 19
Header format
IPv4 addressing
  Subnets and prefixes
  DHCP
  NAT
ICMP
IPv6
Outline

## Slide 20: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”

## Slide 21: DHCP: Dynamic Host Configuration Protocol
Goal: allow host to dynamically obtain an IP address
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile dynamic users
DHCP informs a new host in the network about its:
  IP address
  Subnet mask
  Default gateway
  Address of local DNS server

## Slide 22: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain an IP address
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile dynamic users
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 23: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 24: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!
Notes: Why b/c?
Discover: because the DHCP server’s addr is unknown.
Offer: because the arriving client doesn’t know yet its allocated addresses.
Req: & Ack actually, not necessary. Maybe for informing other hosts and DHCP servers in the network.

## Slide 25: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 26: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 27: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 28: IP addresses: how to get one?
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates addresses
  Assigns domain names, resolves disputes
  Manages DNS

## Slide 29
Header format
IPv4 addressing
  Subnets and prefixes
  DHCP
  NAT
ICMP
IPv6
Outline

## Slide 30: Network Address Translation: Motivation
Lack of IP addresses
Ease work of ISPs
  No need to allocate huge range of addresses, while many of them are actually not in use
  Hierarchical work – decreases complexity
    Separation between change in local network and changes (inc. even changing ISP) in outside world
Devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 31: Network Address Translation
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet

## Slide 32: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 33: NAT: network address translation
16-bit port-number field:
  ~64k simultaneous connections with a single LAN-side address
NAT is controversial:
  Routers should only process up to layer 3
    End-to-end argument
    Address shortage should be solved by IPv6
  NAT disturbs app designers, e.g., P2P apps
    See next slide

## Slide 34: NAT traversal problem
client wants to connect to server with address 10.0.0.1
  server address 10.0.0.1 local to LAN (client can’t use it as destination addr)
  only one externally visible NATed address: 138.76.29.7
solution1: statically configure NAT to forward incoming connection requests at given port to server
  e.g., (123.76.29.7, port 2500) always forwarded to 10.0.0.1 port 25000
10.0.0.1
10.0.0.4
NAT
router
138.76.29.7
client
?

## Slide 35: NAT traversal problem
solution 2: Universal Plug and Play (UPnP) Internet Gateway Device (IGD) Protocol. Allows NATed host to:
  learn public IP address (138.76.29.7)
  add/remove port mappings (with lease times)
10.0.0.1
NAT
router

## Slide 36: NAT traversal problem
solution 3: relaying (used in Skype)
  NATed client establishes connection to relay
  external client connects to relay
  relay bridges packets between to connections
138.76.29.7
client
2. connection to
relay initiated
by NATed host
1. connection to
relay initiated
by client
3. relaying
established
NAT
router
10.0.0.1
Notes: Why cannot the clients continue communicate directly after the connection is established?
Because NAT not only hide theirs addresses / ports from each other, but also disallows every NATed client accepting sessions initiated from outside.
If A connects B directly, that would be a new session.
שיטות אחרות לחציית NAT הן וריאציות שונות על שתי השיטות שראינו – קרי, קינפוג סטטי של נתב ה-NAT, ושימוש בשרת מקשר.

## Slide 37: NAT traversal problem
solution 4:
  Similar to solution 3, but after generating the initial connection, peers communicate directly
  Details
  Bonus HW: generate animation for your lazy lecturer
138.76.29.7
client
2. connection to
relay initiated
by NATed host
1. connection to
relay initiated
by client
3. relaying
established
NAT
router
10.0.0.1

## Slide 38: Is NAT secure?
Is NAT secure?
Notes: Why cannot the clients continue communicate directly after the connection is established?
Because NAT not only hide theirs addresses / ports from each other, but also disallows every NATed client accepting sessions initiated from outside.
If A connects B directly, that would be a new session.
שיטות אחרות לחציית NAT הן וריאציות שונות על שתי השיטות שראינו – קרי, קינפוג סטטי של נתב ה-NAT, ושימוש בשרת מקשר. עם זאת, ישנה שיטה, שבה השרת רק יוצר את ה"היכרות הראשונית" בין המחשבים שמאחורי ה-NATs – ומשם והלאה הם מתקשרים ישירות, ולא דרך השרת. יתכן, שבפועל זה מסתדר כי השרת "מקנפג" את הקצוות או את נתב ה-NAT בהתאם:
http://www.mindcontrol.org/~hplus/nat-punch.html

## Slide 39
IPv4 Header format
IPv4 addressing
Internet Control Message Protocol
IPv6
Outline

## Slide 40: ICMP: internet control message protocol
Usage
  Error reporting
  Checking the network
    Eg, echo (used by ping)
Layer “3.5“
  ICMP msgs carried in IP datagrams
ICMP message
  Type
  Code
  Header & first 8 bytes of the IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header
Notes:   error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)

## Slide 41: Traceroute and ICMP
source sends a series of UDP segments to dest
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
when nth set of datagrams arrives to nth router:
  router discards datagrams
  and sends source ICMP messages (type 11, code 0)
  ICMP messages includes name of router & IP address
when ICMP messages arrives, source records RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes

## Slide 42
IPv4 Header format
IPv4 addressing
Internet Control Message Protocol
IPv6
Outline

## Slide 43: IPv6: motivation
IPv4’s 32-bit address space does not suffice.
IPv4’s header size and format are too varying and complex  hard for speed processing at HW
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 44: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of “flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
Notes: Next header – same as “protocol” in IPv4. Usually, it will be TCP / UDP. However, it may be either merely “options” of IPv4 – that’s a way to have fast-processable-options field.

## Slide 45: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions
Notes: ICMPv6 – contains inside the older IGMP.

## Slide 46: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 47: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 48: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4
Notes: שאלת סטודנט:
כשלמדנו על IP V6 וההתמודדות שלו עם העברת החבילות שלו דרך נתבים שלא תומכים בגרסה זו, הוסבר שהנתב עוטף את החבילה במעטפת של IP V4 ושולח אותו דרך הנתבים,
האם החבילה ממשיכה עד ליעדה בתור חבילה במעטפת של V4? או עד שהיא מגיעה לנתב הראשון שתומך בגרסת V6 והנתב מפרק את החבילה וממשיך לנתב אותה בתור V6? וגם איך הנתב יודע איזה כתובת איי פי לשים במעטפת ה V4 כאשר אין מקום ב header של ה V6 שמכיל את המידע הזה?
תשובה:
יש שיטות רבות, מגוונות ומורכבות ליצירת "מנהרה" לצורך העברת חבילת V6 בתוך V4; הן מפורטות ב-RFC 7059:
https://tools.ietf.org/html/rfc7059
בקצרה, את המנהרה יוצרים לרוב מראש. זה עשוי להיות באמצעות קינפוג ידני, או באמצעות Tunnel Setup Protocol – שבאמצעותו הנתבים שבשני קצוות המנהרה מסכימים ביניהם מראש על הקמת המנהרה. בשני המקרים, מאחר שהמנהרה מוקמת מראש ובמתכוון, ברור שיודעים מהי כתובת ה-V4 שיש לציין בסוף המנהרה; וכן ניתן לבחור ביעילות היכן בדיוק להוציא את חבילת ה-V6 מתוך המעטפת של ה-V4, ולהמשיך לנתב הלאה; בפרט, ניתן, למשל, להשתדל למנוע מצב גרוע שבו אותה חבילת V6 נעטפת בתוך V4 לחלק מסויים מהמסלול, יוצאת מהעטיפה, נכנסת שום למעטפת V4 לחלק נוסף מהמסלול וחוזר חלילה.
בקורס לא נכנסנו לכל הפרטים הנ"ל, והסתפקנו בהיכרות ובתיאור כללי של מנגנון ה"מנהור", שהוא מושג מרכזי ברשתות מחשבים.

## Slide 49: IPv6: adoption
Long (long!) time for deployment, use
  20 years and counting
  think of application-level changes in last 20 years: WWW, Facebook, …
  Why?
Source:
National Institute of Standards and Technology, US Government