## Slide 1: Introduction to data communications Lecturer: Itamar Cohen Lecture 1: Introduction
Vs.
  Teasing question: ADSL is ? time faster than a carrier pigeon.
  Answer
Notes:   Lecture 2, part 1: pkt / circuit switching
  packet Vs. circuit switching
  היום
  היכרות ומנהלה
  מבוא ומושגי יסוד
  מה עשית השבוע וגו’

## Slide 2: Logistics
ofanan@gmail.com, www.ofanan.com
Grading
  Have a look at the syllabus
Appeals for any issue
  By mail only
HWs submission instructions
Always improving…
please print only when necessary
  … and use 2-sided printings

## Slide 3: Course objectives
  Learn basics of data communication and computer networks
  Current & future trends
  Understand HW constraints
Jobs
  Network / Data systems engineers
  Information Technology
  Cyber security
  Application developers
Self study

## Slide 4: Learn how to learn
Repeat the material after every lesson
Don’t leave HWs to the last minute!
Self study
  The course’s textbook
  Google & Wiki
Reception hours
  After the lecture
  Coordinate by mail (Mon-Wed).

## Slide 5: My teaching methodology
Use paper & pencil
  For packets, timing diagrams etc
Simulate
  Small, understandable design
Sanity checks
  Units
  Negative values
Notes:   * Emulate?

## Slide 6: Personal word
My motivation
Your feedback & interest
I don’t know everything…
My aim is to help you to
  succeed in job interviews
  become good engineers
Breaks times

## Slide 7: "כל האומר דבר בשם אומרו" וגו' – A note on the use of these ppt slide
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR.
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
See additional references in the end of each ppt

## Slide 8: Agenda
Acquaintance & administration
What’s the Internet
Network edge
Network core
Optimization criteria
Protocol layers

## Slide 9: The Internet: “nuts and bolts” view
Billions of connected computing devices:
  hosts = end systems
Communication links
  fiber, copper, radio, satellite
Packet switches: forward packets
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
Smartphone
Things
PC
server
wireless
laptop
Notes: 9
ברגים ואומים
* שרת, Server יכול להיות גם מחובר לא ישירות לאינטרנט.
* גם המחשב שלכם יכול להיות שרת
* לא כל רשת חייבת להיות מחוברת לאינטרנט

## Slide 10: What’s the Internet (Cont’)
Internet “network of networks”
  Interconnected ISPs
    Internet Service Providers
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Standards
  IETF: Internet Engineering Task Force
    Publishes RFC: Request for comments

## Slide 11: Internet structure: step by step
Question: how to connect millions of local networks?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Notes: “Welcome 2 the machine”: compare to the development of autonomous cars

## Slide 12: Internet structure: step 1
Full mesh
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
Full Mesh
(Clique):
O(N2)
links

## Slide 13: Internet structure: step 2
Global ISP
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
global ISP

## Slide 14: Internet structure: step 3
Global ISPs (aka tier 1)
  AT&T, Sprint, Level3, …
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
ISP 2
ISP 1
ISP 3
Notes: Step 3: The TIER1 ISPs connect each other, so as to allow global coverage
Step 4: Regional ISPs
Step 5: Finding of lions: Customer, which try to save money, PEER each other
  via IXPs (Internet Exchange Points)
* Finally: Content Provider (e.g., Google, Microsoft, Akamai) appear
  And have their own “nostro” networks

## Slide 15: Internet structure: step by step
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP
Notes: לספר להם את הסיפור עם youtube שאחת החברות רצתה לפתוח את החוזה העברת נתונים
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs

## Slide 16: Real-world tier-1 ISP: Sprint
…
to/from customers
peering
to/from backbone
…
…
…
…
PoP means: “"קצה דרך באחזקת מעצ
POP: point-of-presence

## Slide 17: Other Real-world tier-1 ISPs
Notes: לספר להם על הבעיה ש-youtube יצרה

## Slide 18: Agenda
Acquaintance & administration
What’s the internet
The network edge
  Access network
  Physical media
The network core
Optimization criteria
Protocol layers

## Slide 19: A closer look at network structure:
Network edge
  hosts: clients and servers
    servers often in data centers
  Access networks, communication links
Network core
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 20: The network edge
end systems (hosts):
  run application programs
    e.g. Web, email
  at “edge of network”
client/server model
  client host requests, receives service from always-on server, eg
    Web browser/server
    email client/server
peer-peer model:
  minimal (or no) use of dedicated servers
    e.g. Skype, files sharing
client/server
peer-peer

## Slide 21: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks (school, company)
mobile access networks
Keep in mind:
bandwidth (bits per second) of access network?
shared or dedicated?

## Slide 22: Access net: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wireless access
point
wireless
devices
often combined
in single box
Notes: UFI

## Slide 23: Agenda
Acquaintance & administration
What’s the internet
The network edge
  Access network
  Physical media
The network core
Optimization criteria
Protocol layers

## Slide 24: Access net: Digital Subscriber Line (“Phone netw”)
Central Office
ISP
telephone
network
DSLAM
voice, data transmitted over dedicated link at different freq.
  Asymmetric [down / up] stream rates
  Very-high-bitrate DSL (VDSL)
    Which is, in fact, also asymmetric.
  The de-facto speed is affected by
    Distance to the CO
    Gauge of the cable
    Electro-Magnetic Interference
    How much the costumer paid
DSL
modem
splitter
DSL Access
Multiplexer
Notes: Modem – converts D (from the PC) to Analog. The DSLAM converts it back to digital, multiplexing multiple users.

## Slide 25: Access net: cable network (Hot)
data, TV transmitted at different
frequencies over a shared cable
cable
modem
splitter
…
cable headend

## Slide 26: Access net: cable network (hot)
cable
modem
splitter
…
cable headend
Channels
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
V
I
D
E
O
D
A
T
A
D
A
T
A
C
O
N
T
R
O
L
1
2
3
4
5
6
7
8
9
Notes: frequency division multiplexing: different channels transmitted
in different frequency bands

## Slide 27: Access net: cable network (hot)
Data Over Cable Service Interface Specification
High BW (DOCSIS 3.1: 1/10Gbps up/downstream), but
  BW may be divided to multiple heavy users
  BW is subject to physical / financial constraints , similar to DSL
data, TV transmitted at different
frequencies over shared cable
cable
modem
splitter
…
cable headend
ISP
Cable Modem
Termination System

## Slide 28: Fiber To The X
Q: how close to the desktop can the fiber get?
A: either to the
  Node / Neighborhood
    Hybrid Fiber Cable
  Cabinet
  Building
  Home
  Desktop

## Slide 29: Enterprise access networks (Ethernet)
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)
Typically used in companies, universities, etc
  Rates: 10M / 100M / 1G / 10Gbps …

## Slide 30: Wireless access networks
shared wireless access network connects end system to router
  Via Base Station (aka Access Point)
Wireless LANs:
    within building (100 ft)
    802.11b/g (WiFi)
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  3G, 4G, 5G
to Internet
to Internet

## Slide 31: Physical Media: guided media
Twisted pair
  aka ביסלי גריל
  Why twist?
  Made of copper
  Either shielded
  …or Unshielded
Coaxial cable
  Coaxial means: בעל ציר משותף
  In aim to decrease outer EMI
  Common in cable TV

## Slide 32: Physical guided media: Fiber optic cable
 Very fast: ~100 Gbps
  Standards are named OC-n (Optical Carrier), where OC-1 carries 51.8 Mbps
    So the BW of OC-768 is ~40Gbps
 Very low signal attenuation, even for ~100km
 Very expensive
  Not necessarily the cables themselves, but – the xmt/rcvrs and switches

## Slide 33: Physical unguided media: radio
Signal carried in electromagnetic spectrum
propagation environment effects:
  Reflection
  Obstacles
  Interference
Can be classified by the distances
  Very short distances (keyboard, mouse, earphones)
  Medium distances: Wireless Local Area Network
    WiFi
  Wide are networks
    4G, 5G cellular
  Satellite
    Geostationary: 36K kms above earth
    Low-Earth Orbiting
    Significant propagation delay

## Slide 34: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
  Packet switching
  Circuit switching
Optimization criteria
Protocol layers

## Slide 35: Packet switching
Hosts break application-layer messages into packets
  Forward packets from one router to the next across links on path from source to destination
  Each packet transmitted at full link capacity
  Either source routing, or fixing only the next-hop

## Slide 36
http://www.adalovelace.com
001100
011001
011001
11011
110101
Ada Lovelace
http://www.adalovelace.com
Animation by: Nick McKeown &
Balaji Prabhakar
Pros. & Cons.?

## Slide 37: Packet switching: transmission rate
Denote:
  packet length L
  transmission rate R
    Aka link capacity, link bandwidth
    Fixed by the (bottleneck) link
packet
transmission
delay
time needed to
transmit L-bit
packet into link
L (bits)
R (bits/sec)
=
=

## Slide 38: Packet-switching: store-and-forward
Entire packet must arrive at router before it can be transmitted on next link
source
R bps
destination
1
2
3
L bits
per packet
R bps

## Slide 39: Packet-switching: queuing delay & loss
If arrival rate > xmt rate, packets will queue
Packets may be dropped (lost) if buffer is full
A
B
C
R = 100 Mb/s
R = 30 Mb/s
D
E
queue of packets
waiting for output link

## Slide 40: Forwarding & Routing
Routing: determines source-destination route taken by packets
  routing algorithms
Forwarding: move packets from router’s input to appropriate router output
Forwarding table
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 41: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
  Packet switching
  Circuit switching
Optimization criteria
Protocol layers

## Slide 42: Transportation analogy
Routing alg: WAZE
Fwd. table: what to do in the next interchange
Circuit switching: rails

## Slide 43: Circuit switching
End-end resources allocated & reserved for “call” between source & dest:
  Guaranteed performance
circuit segment idle (and wasted) if not used by call
  no sharing
Used in traditional telephone networks
Notes: מירי רגב מדברת בטל' עם מתי כספי

## Slide 44: Circuit switching: FDM & TDM
Freq
Division
Multiplexing
frequency
time
frequency
time
4 users
Example:
Time
Division
Multiplexing
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.

## Slide 45: Packet Vs. circuit switching
Packet switching
   Great for bursty data
   Resource sharing
   No call setup
   No BW guarantees - excessive congestion possible
   Packet delay and loss
   Protocols needed for reliable data transfer, congestion control

## Slide 46: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
Optimization criteria
  Power
  Delay
  Throughput
  Packet loss
Protocol layers

## Slide 47: Power saving: motivation
Save power  Less diseases and death from polluting power plants
Save money
  Electrical bills
  Cooling costs
Battery life
Heat of devices
  Inconvenient to the human user
  Causes electrical problems

## Slide 48: Green networking: industrial projects
Source: Alcatel-Lucent Eco-Sustainable Networks

## Slide 49: Big router is not a matchbox
Cisco GSR 12816
Juniper T640
2m
50 cm
60cm
Capacity: 640Gb/s Power: 5kW
1m
75 cm
50 cm
Capacity: 320Gb/s Power: 3kW

## Slide 50: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
Optimization criteria
  Power
  Delay
  Throughput
  Packet loss
Protocol layers
Notes: למי כאן יש רשיון לאופנוע?

## Slide 51: Four sources of packet delay
dproc – depended upon the network equipment and the concrete packet’s characteristics
dqueue – depended upon link congestion
dtrans – depended upon pkt size & link rate
dprop – depended upon distance & (hopefully) speed of light
node
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
propagation
transmission

## Slide 52: Delay: notations
Dproc + dqueue – aka Tproc, TD
dtra – aka Ttrans, Txmt, or Tx
dprop – aka Tpd
Notes: Mb  this is contrast to Mebibit=2^20 bits

## Slide 53: Packet delay: Kahoot.it
מעבירים חבילת מידע יחידה מארה"ב לאב"ג, דרך נתב יחיד. נתונים:
Pkt size: 12.5kBytes
Link rates: 100 Mbps
Distance: 20,000 kms
Propagation speed: 2*10^8 mps
Tproc = 1 ms
Tq = 0
כמה זמן עובר מרגע שמתחילים לשדר את החבילה בארה"ב, ועד שהיא מגיעה במלואה ליעד באב"ג?

## Slide 54: Packet delay: numerical example
dproc + dqueue  100 nsec
dxmt – 12.5kB packet @ 100 Mbps 
dprop – 20k km @ 2*10^8 m/sec 
node
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
propagation
transmission
Notes: Dxmt: 12.5kB / 100 Mbps = 100 kb / 100 Mbps = 1 ms
Dprop: 20k kms = 20*10^6 m = 2*10^7 m  Dprop = 0.1 sec
2*Txmt + Tprop + Tproc + Tq = 2*100kb / 100 Mbps + 20 Mm / 2*10^8 mps + 1 ms =
= 2 ms + (20 / 200) s + 1 ms = 103 ms.

## Slide 55: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
Optimization criteria
  Power
  Delay
  Throughput
  Packet loss
Protocol layers

## Slide 56: Throughput
Throughput: rate (bits/sec) at which bits transferred between sender/receiver
Goodput: rate of the useful data
  Eg, the file sent – excluding headers & trailers
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec
pipe that can carry
fluid at rate
Rc bits/sec

## Slide 57: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
Optimization criteria
  Power
  Delay
  Throughput
  Packet loss
Protocol layers

## Slide 58: Packet loss
Queue (aka buffer) preceding link has finite capacity
Packet arriving to (almost) full queue may be dropped (aka lost, rejected, discarded)
Upon realizing that a packet was lost, the source node / previous node may retransmit it
A
B
packet being transmitted
packet arriving to
a full buffer is lost
buffer
(waiting area)

## Slide 59: Agenda
Acquaintance & administration
What’s the internet
Network edge
Network core
Optimization criteria
  Power
  Delay
  Throughput
  Packet loss
Protocol layers

## Slide 60: Protocol “Layers”
Networks are complex!
many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
Is there any hope of organizing structure of network?

## Slide 61: Internet Layers: a postal service analogy
Application: online purchase
Transport: express / registered / regular
Network: Use WAZE to find best route
link: Terminal’s gate, interchange exit
physical: Conveyor belt / crane / porters
application
transport
network
link
physical

## Slide 62: Why layering?
Hierarchical, top-down planning
  Divide a complex task to smaller, easier tasks.
Easier maintenance
  A change of implementation of layer’s service is transparent to rest of system

## Slide 63: Breaking data in segments
Data

## Slide 64: The complete packet
Application Header
Presentation Header
Session Header
Transport Header
Network Header
Link Header
Frame Preamble
Data Link Trailer(CRC)
Data
Packet

## Slide 65: Packet creation process
Data
Data
65
Introduction 1-65

## Slide 66: Internet protocol stack
Why “Stack”?
Application: e.g. e-mail, web, file sharing
Transport: (un)reliable proc.-to-proc. data transfer
Network: end-to-end routing
Link: transfer between neighboring nodes
Physical: bits “on the wire”
application
transport
network
link
physical
Notes: Physical: See
https://en.wikipedia.org/wiki/Line_code

## Slide 67: OSI reference model (by ISO)
OSI: Open Source Interconnection
ISO: International Organization for Standardization
presentation: allow applications to interpret meaning of data, e.g., encryption, compression
session: synchronization.
  Eg: migration
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
application
presentation
session
transport
network
link
physical

## Slide 68: OSI model

## Slide 69: The 5 / 7 layers
Notes: L5
Simple Mail Trans’ Prot’.
Domain Name System.
HyperText Transfer Prot’.
Simple Netw. Mgmt. Prot’.
L4
UDP (User Datagram Prot’) assumes that error checking and correction is either not necessary or performed in the application, avoiding the overhead of such processing at the network interface level. Time-sensitive applications often use UDP because dropping packets is preferable to waiting for delayed packets, which may not be an option in a real-time system.
UDP's stateless nature is also useful for servers answering small queries from huge numbers of clients. Unlike TCP, UDP supports packet broadcast (sending to all on local network) and multicasting (send to all subscribers).
UDP is used for DNS, streaming media (IPTV, VoIP) and online games.
TCP (Transmission Ctrl Prot’).
SCTP (Stream Ctrl Transmission Prot’) – provides reliability, sequencing and cong. ctrl. as in TCP; SCTP is msg-oriented, as is UDP.
L3
I Group Management Prot.
Other Network Layer Protocols:
IPSec (Secure).
Routing protocols (BGP, RIP, OSPF).

## Slide 70: Why NOT layering?
In practice, the borders between the layers are not definite
  The “link layer” of delivery (flight / boat / car) impacts the higher layers
Layering considered harmful
  Duplicate functions (eg ECC / Checksum)
    Parallel to multiple identical security checks at an airport
Knowledge about other layers may enable optimizations
  Eg – is there another branch of the destination company in case of a traffic jam?

## Slide 71: Conclusion
Communication networks are imperfect
Many problems stem from “historical reasons”

## Slide 72: References
EE384x, Packet Switch Architectures – lectures slides by Nick McKeown & Balaji Prabakhar, spring 2012, Stanford University